## Slide 1: CS162 Operating Systems and Systems Programming Lecture 17 Performance Storage Devices, Queueing Theory
May 31st, 2020
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: How the processor talks to the device
CPU interacts with a Controller
  Contains a set of registers that can be read and written
  May contain memory for request queues or bit-mapped images
Regardless of the complexity of the connections and buses, processor accesses registers in two ways:
  I/O instructions: in/out instructions
    Example from the Intel architecture: out 0x21,AL
  Memory mapped I/O: load/store instructions
    Registers/memory appear in physical address space
    I/O accomplished with load and store instructions
Device Controller
read
write
control
status
Addressable
Memory
and/or
Queues
Registers
(port 0x20)
Hardware
Controller
Memory Mapped
Region: 0x8F008020
Bus
Interface
Address +
Data
Interrupt Request
Processor Memory Bus
CPU
Regular
Memory
Interrupt
Controller
Bus
Adaptor
Bus
Adaptor
Other Devices
or Buses

## Slide 3: Recall: Memory-Mapped Display Controller
Memory-Mapped:
  Hardware maps control registers and display memory into physical address space
    Addresses set by HW jumpers or at boot time
  Simply writing to display memory (also called the “frame buffer”) changes image on screen
    Addr: 0x8000F000 — 0x8000FFFF
  Writing graphics description to cmd queue
    Say enter a set of triangles describing some scene
    Addr: 0x80010000 — 0x8001FFFF
  Writing to the command register may cause on-board graphics hardware to do something
    Say render the above scene
    Addr: 0x0007F004
Can protect with address translation
Display
Memory
0x8000F000
0x80010000
Physical
Address
Space
Status
0x0007F000
Command
0x0007F004
Graphics
Command
Queue
0x80020000

## Slide 4: Transferring Data To/From Controller
Programmed I/O:
  Each byte transferred via processor in/out or load/store
  Pro: Simple hardware, easy to program
  Con: Consumes processor cycles proportional to data size
Direct Memory Access:
  Give controller access to memory bus
  Ask it to transfer data blocks to/from memory directly
Sample interaction with DMA controller (from OSC book):
1
2
3

## Slide 5: Transferring Data To/From Controller
Programmed I/O:
  Each byte transferred via processor in/out or load/store
  Pro: Simple hardware, easy to program
  Con: Consumes processor cycles proportional to data size
Direct Memory Access:
  Give controller access to memory bus
  Ask it to transfer data blocks to/from memory directly
Sample interaction with DMA controller (from OSC book):
4
5
6

## Slide 6: I/O Device Notifying the OS
The OS needs to know when:
  The I/O device has completed an operation
  The I/O operation has encountered an error
I/O Interrupt:
  Device generates an interrupt whenever it needs service
  Pro: handles unpredictable events well
  Con: interrupts relatively high overhead
Polling:
  OS periodically checks a device-specific status register
    I/O device puts completion information in status register
  Pro: low overhead
  Con: may waste many cycles on polling if infrequent or unpredictable I/O operations
Actual devices combine both polling and interrupts
  For instance – High-bandwidth network adapter:
    Interrupt for first incoming packet
    Poll for following packets until hardware queues are empty
Notes: After the OS has issued a command to the I/O device either via a special I/O instruction or by writing to a location in the I/O address space, the OS needs to be notified when:
(a) The I/O device has completed the operation.
(b) Or when the I/O device has encountered an error.
This can be accomplished in two different ways: Polling and I/O interrupt.
+1 = 58 min. (Y:38)

## Slide 7: Device Drivers
Device Driver: Device-specific code in the kernel that interacts directly with the device hardware
  Supports a standard, internal interface
  Same kernel I/O system can interact easily with different device drivers
  Special device-specific configuration supported with the ioctl() system call
Device Drivers typically divided into two pieces:
  Top half: accessed in call path from system calls
    implements a set of standard, cross-device calls like open(), close(), read(), write(), ioctl(), strategy()
    This is the kernel’s interface to the device driver
    Top half will start I/O to device, may put thread to sleep until finished
  Bottom half: run as interrupt routine
    Gets input or transfers next block of output
    May wake sleeping threads if I/O now complete

## Slide 8: Life Cycle of An I/O Request
Device Driver
Top Half
Device Driver
Bottom Half
Device
Hardware
Kernel I/O
Subsystem
User
Program

## Slide 9: Basic Performance Concepts
Response Time or Latency: Time to perform an operation(s)
Bandwidth or Throughput: Rate at which operations are performed (op/s)
  Files: MB/s, Networks: Mb/s, Arithmetic: GFLOP/s
Start up or “Overhead”: time to initiate an operation
Most I/O operations are roughly linear in b bytes
  Latency(b) = Overhead + b/TransferCapacity

## Slide 10: Example (Fast Network)
Consider a 1 Gb/s link (BW = 125 MB/s)
  With a startup cost S = 1 ms
  Latency(b) = S + b/BW
  Bandwidth = b/(S + b/BW) = BWb/(BWS + b) = BW/(BWS/b + 1)

## Slide 11: Example (Fast Network)
Consider a 1 Gb/s link (BW = 125 MB/s)
  With a startup cost S = 1 ms
  Half-power Bandwidth  BW/(BW*S/b + 1) = BW/2
  Half-power point occurs at b= S*BW = 125,000 bytes

## Slide 12: Example: at 10 ms startup (like Disk)
  Half-power b = 1,250,000 bytes!

## Slide 13: What Determines Peak BW for I/O ?
Bus Speed
  PCI-X: 1064 MB/s = 133 MHz x 64 bit (per lane)
  ULTRA WIDE SCSI: 40 MB/s
  Serial ATA & IEEE 1394 (firewire): 1.6 Gb/s full duplex (200MB/s)
  SAS-1: 3 Gb/s, SAS-2: 6 Gb/s, SAS-3: 12 Gb/s, SAS-4: 22.5 GB/s
  USB 3.0 – 5 Gb/s
  Thunderbolt 3 – 40 Gb/s
Device Transfer Bandwidth
  Rotational speed of disk
  Write / Read rate of NAND flash
  Signaling rate of network link
Whatever is the bottleneck in the path…

## Slide 14: Storage Devices
Magnetic disks
  Storage that rarely becomes corrupted
  Large capacity at low cost
  Block level random access (except for SMR – later!)
  Slow performance for random access
  Better performance for sequential access
Flash memory
  Storage that rarely becomes corrupted
  Capacity at intermediate cost (5-20x disk)
  Block level random access
  Good performance for reads; worse for random writes
  Erasure requirement in large blocks
  Wear patterns issue

## Slide 15: Hard Disk Drives (HDDs)
IBM/Hitachi Microdrive
Western Digital Drive
http://www.storagereview.com/guide/
Read/Write Head
Side View
IBM Personal Computer/AT (1986)
  30 MB hard disk - $500
  30-40ms seek time
  0.7-1 MB/s (est.)
Notes: Winchester disk drives developed by IBM: 1973 first drive
Uses “sealed” assembly with heads floating on air bearings – Bernoulli effect

## Slide 16: The Amazing Magnetic Disk
Unit of Transfer: Sector
  Ring of sectors form a track
  Stack of tracks form a cylinder
  Heads position on cylinders
Disk Tracks ~ 1µm (micron) wide
  Wavelength of light is ~ 0.5µm
  Resolution of human eye: 50µm
  100K tracks on a typical 2.5” disk
Separated by unused guard regions
  Reduces likelihood neighboring tracks are corrupted during writes (still a small non-zero chance)

## Slide 17: The Amazing Magnetic Disk
Track length varies across disk
  Outside: More sectors per track, higher bandwidth
  Disk is organized into regions of tracks with same # of sectors/track
  Only outer half of radius is used
    Most of the disk area in the outer regions of the disk
Disks so big that some companies (like Google) reportedly only use part of disk for active data
  Rest is archival data

## Slide 18: Shingled Magnetic Recording (SMR)
Overlapping tracks yields greater density, capacity
Restrictions on writing, complex DSP for reading
Examples: Seagate (8TB), Hitachi (10TB)

## Slide 19: Review: Magnetic Disks
Cylinders: all the tracks under the head at a given point on all surface
Read/write data is a three-stage process:
  Seek time: position the head/arm over the proper track
  Rotational latency: wait for desired sector to rotate under r/w head
  Transfer time: transfer a block of bits (sector) under r/w head
Sector
Track
Cylinder
Head
Platter
Seek time = 4-8ms
One rotation = 8-16ms (3600-7200 RPM)

## Slide 20: Review: Magnetic Disks
Cylinders: all the tracks under the head at a given point on all surface
Read/write data is a three-stage process:
  Seek time: position the head/arm over the proper track
  Rotational latency: wait for desired sector to rotate under r/w head
  Transfer time: transfer a block of bits (sector) under r/w head
Sector
Track
Cylinder
Head
Platter
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
Disk Latency = Queueing Time + Controller time +
Seek Time + Rotation Time + Xfer Time

## Slide 21: Typical Numbers for Magnetic Disk
Parameter | Info / Range
Space/Density | Space: 14TB (Seagate), 8 platters, in 3½ inch form factor! Areal Density: ≥ 1Terabit/square inch! (PMR, Helium, …)
Average seek time | Typically 4-6 milliseconds. Depending on reference locality, actual cost may be 25-33% of this number.
Average rotational latency | Most laptop/desktop disks rotate at 3600-7200 RPM (16-8 ms/rotation). Server disks up to 15,000 RPM. Average latency is halfway around disk so 8-4 milliseconds
Controller time | Depends on controller hardware
Transfer time | Typically 50 to 250 MB/s. Depends on: Transfer size (usually a sector): 512B – 1KB per sector Rotation speed: 3600 RPM to 15000 RPM Recording density: bits per inch on a track Diameter: ranges from 1 in to 5.25 in
Cost | Used to drop by a factor of two every 1.5 years (or even faster); now slowing down
Notes: As far as rotational latency is concerned, most disks rotate at 3,600 RPM or approximately 16 ms per revolution.
Since on average, the information you desired is half way around the disk, the average rotational latency will be 8ms.
The transfer time is a function of transfer size, rotation speed, and recording density.
The typical transfer speed is 2 to 4 MB per second.
Notice that the transfer time is much faster than the rotational latency and seek time.
This is similar to the DRAM situation where the DRAM access time is much shorter than the DRAM cycle time.
***** Do anybody remember what we did to take advantage of the short access time versus cycle time? Well, we interleave!
New International Disk Drive, Equipment, and Materials Association standard is 4KB sectors instead of 512 byte sectors
+2 = 36 min. (Y:16)

## Slide 22: Disk Performance Example
Assumptions:
  Ignoring queuing and controller times for now
  Avg seek time of 5ms,
  7200RPM  Time for rotation: 60000 (ms/min) / 7200(rev/min) ~= 8ms
  Transfer rate of 50MByte/s, block size of 4Kbyte  4096 bytes/50×106 (bytes/s) = 81.92 × 10-6 sec  0.082 ms for 1 sector
Read block from random place on disk:
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.082ms) = 9.082ms
  Approx 9ms to fetch/put data: 4096 bytes/9.082×10-3 s  451KB/s
Read block from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.082ms) = 4.082ms
  Approx 4ms to fetch/put data: 4096 bytes/4.082×10-3 s  1.03MB/s
Read next block on same track:
  Transfer (0.082ms): 4096 bytes/0.082×10-3 s  50MB/sec
Key to using disk effectively (especially for file systems) is to minimize seek and rotational delays

## Slide 23: (Lots of) Intelligence in the Controller
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops
…

## Slide 24: Hard Drive Prices over Time

## Slide 25: Example of Current HDDs
Seagate Exos X14 (2018)
  14 TB hard disk
    8 platters, 16 heads
    Helium filled: reduce friction and power
  4.16ms average seek time
  4096 byte physical sectors
  7200 RPMs
  6 Gbps SATA /12Gbps SAS interface
    261MB/s MAX transfer rate
    Cache size: 256MB
  Price: $615 (< $0.05/GB)
IBM Personal Computer/AT (1986)
  30 MB hard disk
  30-40ms seek time
  0.7-1 MB/s (est.)
  Price: $500 ($17K/GB, 340,000x more expensive !!)

## Slide 26: Solid State Disks (SSDs)
1995 – Replace rotating magnetic media with non-volatile memory (battery backed DRAM)
2009 – Use NAND Multi-Level Cell (2 or 3-bit/cell) flash memory
  Sector (4 KB page) addressable, but stores 4-64 “pages” per memory block
  Trapped electrons distinguish between 1 and 0
No moving parts (no rotate/seek motors)
  Eliminates seek and rotational delay (0.1-0.2ms access time)
  Very low power and lightweight
  Limited “write cycles”
Rapid advances in capacity and cost ever since!

## Slide 27: SSD Architecture – Reads
  Read 4 KB Page: ~25 usec
  No seek or rotational latency
  Transfer time: transfer a 4KB page
    SATA: 300-600MB/s => ~4 x103 b / 400 x 106 bps => 10 us
  Latency = Queuing Time + Controller time + Xfer Time
  Highest Bandwidth: Sequential OR Random reads
Host
Buffer
Manager
(software
Queue)
Flash
Memory
Controller
DRAM
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
SATA

## Slide 28: SSD Architecture – Writes
  Writing data is complex! (~200μs – 1.7ms )
  Can only write empty pages in a block
  Erasing a block takes ~1.5ms
  Controller maintains pool of empty blocks by coalescing used pages (read, erase, write), also reserves some % of capacity
Rule of thumb: writes 10x reads, erasure 10x writes
https://en.wikipedia.org/wiki/Solid-state_drive

## Slide 29: Some “Current” 3.5in SSDs
Seagate Nytro SSD: 15TB (2017)
  Dual 12Gb/s interface
  Seq reads 860MB/s
  Seq writes 920MB/s
  Random Reads (IOPS): 102K
  Random Writes (IOPS): 15K
  Price (Amazon): $6325 ($0.41/GB)
Nimbus SSD: 100TB (2019)
  Dual port: 12Gb/s interface
  Seq reads/writes: 500MB/s
  Random Read Ops (IOPS): 100K
  Unlimited writes for 5 years!
  Price: ~ $50K? ($0.50/GB)

## Slide 30: HDD vs SSD Comparison
SSD prices drop much faster than HDD

## Slide 31: Amusing calculation: Is a full Kindle heavier than an empty one?
Actually, “Yes”, but not by much
Flash works by trapping electrons:
  So, erased state lower energy than written state
Assuming that:
  Kindle has 4GB flash
  ½ of all bits in full Kindle are in high-energy state
  High-energy state about 10-15 joules higher
  Then: Full Kindle is 1 attogram (10-18gram) heavier (Using E = mc2)
Of course, this is less than most sensitive scale can measure (it can measure 10-9 grams)
Of course, this weight difference overwhelmed by battery discharge, weight from getting warm, ….
Source: John Kubiatowicz (New York Times, Oct 24, 2011)

## Slide 32: SSD Summary
Pros (vs. hard disk drives):
  Low latency, high throughput (eliminate seek/rotational delay)
  No moving parts:
    Very light weight, low power, silent, very shock insensitive
  Read at memory speeds (limited by controller and I/O bus)
Cons
  Small storage (0.1-0.5x disk), expensive (3-20x disk)
    Hybrid alternative: combine small SSD with large HDD

## Slide 33: SSD Summary
Pros (vs. hard disk drives):
  Low latency, high throughput (eliminate seek/rotational delay)
  No moving parts:
    Very light weight, low power, silent, very shock insensitive
  Read at memory speeds (limited by controller and I/O bus)
Cons
  Small storage (0.1-0.5x disk), expensive (3-20x disk)
    Hybrid alternative: combine small SSD with large HDD
  Asymmetric block write performance: read pg/erase/write pg
    Controller garbage collection (GC) algorithms have major effect on performance
  Limited drive lifetime
    1-10K writes/page for MLC NAND
    Avg failure rate is 6 years, life expectancy is 9–11 years
These are changing rapidly!
No longer true!

## Slide 34: Nano-Tube Memory (NANTERO)
Yet another possibility: Nanotube memory
  NanoTubes between two electrodes, slight conductivity difference between ones and zeros
  No wearout!
Better than DRAM?
  Speed of DRAM, no wearout, non-volatile!
  Nantero promises 512Gb/dice for 8Tb/chip! (with 16 die stacking)

## Slide 35: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW per op = transfer size / response time
    EffBW(n) = n / (S + n/B) = B / (1 + SB/n )
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%
# of ops
Fixed overhead
time per op

## Slide 36: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW per op = transfer size / response time
    EffBW(n) = n / (S + n/B) = B / (1 + SB/n )
  Contributing factors to latency:
    Software paths (can be loosely modeled by a queue)
    Hardware controller
    I/O device service time
Queuing behavior:
  Can lead to big increases of latency as utilization increases
  Solutions?
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 37: A Simple Deterministic World
Assume requests arrive at regular intervals, take a fixed time to process, with plenty of time between …
Service rate (μ = 1/TS) - operations per second
Arrival rate: (λ = 1/TA) - requests per second
Utilization: U = λ/μ , where λ < μ
Average rate is the complete story
Queue
Server
arrivals
departures
TQ
TS
TA
TA
TA
TS
Tq

## Slide 38: A Ideal Linear World
What does the queue wait time look like?
  Grows unbounded at a rate ~ (Ts/TA) till request rate subsides
Offered Load (TS/TA)
Delivered Throughput
0
1
1
time
Queue delay
Delivered Throughput
0
1
1
Offered Load (TS/TA)
Empty Queue
Saturation
Unbounded
time
Queue delay

## Slide 39: A Bursty World
Requests arrive in a burst, must queue up till served
Same average arrival time, but almost all of the requests experience large queue delays
Even though average utilization is low
Queue
Server
arrivals
departures
TQ
TS
Q depth
Server
Arrivals

## Slide 40: So how do we model the burstiness of arrival?
Elegant mathematical framework if you start with exponential distribution
  Probability density function of a continuous random variable with a mean of 1/λ
  f(x) = λe-λx
  “Memoryless”
Chart: 
| 1E-3 | 0.01 | 0.02 | 0.04 | 0.08 | 0.16 | 0.32 | 0.64 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 10
f(x) | 0.999 | 0.99005 | 0.9802 | 0.96079 | 0.92312 | 0.85214 | 0.72615 | 0.52729 | 0.36788 | 0.13534 | 0.049787 | 0.018316 | 0.0067379 | 0.0024788 | 0.00091188 | 0.00033546 | 4.54e-05
Likelihood of an event occurring is independent of how long we’ve been waiting
Lots of short arrival intervals (i.e., high instantaneous rate)
Few long gaps (i.e., low instantaneous rate)
x (λ)
mean arrival interval (1/λ)

## Slide 41: Background: General Use of Random Distributions
Server spends variable time (T) with customers
  Mean (Average) m = p(T)T
  Variance (stddev2) 2 = p(T)(T-m)2 = p(T)T2-m2
  Squared coefficient of variance: C = 2/m2 Aggregate description of the distribution
Important values of C:
  No variance or deterministic  C=0
  “Memoryless” or exponential  C=1
    Past tells nothing about future
    Poisson process – purely or completely random process
    Many complex systems (or aggregates) are well described as memoryless
  Disk response times C  1.5 (majority seeks < average)
Mean
(m)
mean
Memoryless
Distribution
of service times


## Slide 42: Introduction to Queuing Theory
Departures
Arrivals
Queuing System
What about queuing time??
  Let’s apply some queuing theory
  Queuing Theory applies to long term, steady state behavior  Arrival rate = Departure rate
Arrivals characterized by some probabilistic distribution
Departures characterized by some probabilistic distribution
Queue
Controller
Disk
Notes: Old and New Testament by Kleirock
Regret skipping as grad student

## Slide 43: Little’s Law
In any stable system
  Average arrival rate = Average departure rate
The average number of jobs/tasks in the system (N) is equal to arrival time / throughput (λ) times the response time (L)
  N (jobs) = λ (jobs/s) x L (s)
Regardless of structure, bursts of requests, variation in service
  Instantaneous variations, but it washes out in the average
  Overall, requests match departures
arrivals
departures
N
λ
L

## Slide 44: Example
λ = 1
L = 5
0
1
2
3
4
5
6
7
8
16
9
10
11
12
13
14
15
time
Jobs
L = 5
N = 5 jobs
A: N = λ x L
E.g., N = λ x L = 5

## Slide 45: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
Job i
L(1)

## Slide 46: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
What is the system occupancy, i.e., average
number of jobs in the system?
Job i

## Slide 47: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
S = S(1) + S(2) + … + S(k) = L(1) + L(2) + … + L(k)
S(k)

## Slide 48: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Average occupancy (Navg) = S/T
Job i
S= area

## Slide 49: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = S/T = (L(1) + … + L(k))/T
S(k)

## Slide 50: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = (L(1) + … + L(k))/T = (Ntotal/T)*(L(1) + … + L(k))/Ntotal
S(k)

## Slide 51: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = (Ntotal/T)*(L(1) + … + L(k))/Ntotal = λavg × Lavg
S(k)

## Slide 52: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = λavg × Lavg
S(k)

## Slide 53: A Little Queuing Theory: Some Results
Assumptions:
  System in equilibrium; No limit to the queue
  Time between successive arrivals is random and memoryless
Parameters that describe our system:
  : mean number of arriving customers/second
  Tser: mean time to service a customer (“m1”)
  C: squared coefficient of variance = 2/m12
  μ: service rate = 1/Tser
  u: server utilization (0u1): u = /μ =   Tser
Parameters we wish to compute:
  Tq: Time spent in queue
  Lq: Length of queue =   Tq (by Little’s law)
Results:
  Memoryless service distribution (C = 1): (an “M/M/1 queue”):
    Tq = Tser x u/(1 – u)
  General service distribution (no restrictions), 1 server (an “M/G/1 queue”):
    Tq = Tser x ½(1+C) x u/(1 – u)
Arrival Rate

Queue
Server
Service Rate
μ=1/Tser
Why does response/queueing delay grow unboundedly even though the utilization is < 1 ?
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 54: Why unbounded response time?
Assume deterministic arrival process and service time
  Possible to sustain utilization = 1 with bounded response time!
time
arrival time
service time

## Slide 55: Why unbounded response time?
Assume stochastic arrival process (and service time)
  No longer possible to achieve utilization = 1
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%
time
This wasted time can never be reclaimed! So cannot achieve u = 1!

## Slide 56: A Little Queuing Theory: An Example
Example Usage Statistics:
  User requests 10 x 8KB disk I/Os per second
  Requests & service exponentially distributed (C=1.0)
  Avg. service = 20 ms (From controller+seek+rot+trans)
Questions:
  How utilized is the disk?
    Ans: server utilization, u = Tser
  What is the average time spent in the queue?
    Ans: Tq
  What is the number of requests in the queue?
    Ans: Lq
  What is the avg response time for disk request?
    Ans: Tsys = Tq + Tser
Computation:
 (avg # arriving customers/s) = 10/s
Tser (avg time to service customer) = 20 ms (0.02s)
u (server utilization) =  x Tser= 10/s x .02s = 0.2
Tq (avg time/customer in queue) = Tser x u/(1 – u) = 20 x 0.2/(1-0.2) = 20 x 0.25 = 5 ms (0 .005s)
Lq (avg length of queue) =  x Tq=10/s x .005s = 0.05
Tsys (avg time/customer in system) =Tq + Tser= 25 ms

## Slide 57: Queuing Theory Resources
Resources page contains Queueing Theory Resources (under Readings):
  Scanned pages from Patterson and Hennessy book that gives further discussion and simple proof for general equation: https://cs162.eecs.berkeley.edu/static/readings/patterson_queue.pdf
  A complete website full of resources: http://web2.uwindsor.ca/math/hlynka/qonline.html
Some previous midterms with queueing theory questions
Assume that Queueing Theory is fair game for Midterm III!

## Slide 58: Summary
Disk Performance:
  Queuing time + Controller + Seek + Rotational + Transfer
  Rotational latency: on average ½ rotation
  Transfer time: spec of disk depends on rotation speed and bit storage density
Devices have complex interaction and performance characteristics
  Response time (Latency) = Queue + Overhead + Transfer
    Effective BW = BW * T/(S+T)
  HDD: Queuing time + controller + seek + rotation + transfer
  SDD: Queuing time + controller + transfer (erasure & wear)
Systems (e.g., file system) designed to optimize performance and reliability
  Relative to performance characteristics of underlying device
Bursts & High Utilization introduce queuing delays
Queuing Latency:
  M/M/1 and M/G/1 queues: simplest to analyze
  As utilization approaches 100%, latency  
  Tq = Tser x ½(1+C) x u/(1 – u))